## Slide 1
Vessel Schedule Recovery Problem
Extensions, Benchmarking & Regulatory Compliance
①
Baseline Completion
②
CO₂ & Regulatory
③
Solver Benchmarking
④
CFA Policy

## Slide 2
Agenda
TJL Optimization | VSRP Extensions & Benchmarking | 2026
1
Problem Background
Maritime disruption context, VSRP definition, recovery strategies
2
Mathematical Model
MIP formulation, variables, constraints, objective function
3
Implementation
Solver-agnostic architecture, swap groups, transshipment logic
4
Sensitivity Analysis
Alpha trade-off frontier, delay sweep, green recovery tension
5
Emissions & Regulation
EU ETS, IMO CII, FuelEU Maritime, stochastic carbon price
6
Solver Benchmarking
Xpress vs HiGHS vs CBC — solution quality, runtime, stability
7
CFA Policy
Additive, decay, SPSA update rules — tail risk and service reliability
8
Penalty Sensitivity
Swap and speed-up penalty thresholds across random seeds
9
Conclusions
Key findings, limitations, future work

## Slide 3
Problem Background
Maritime transportation and schedule disruptions
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Maritime Context
• 80% of global trade volume moves by sea
• Liner shipping: fixed routes, public schedules
• 70–80% of voyages experience delays
• Just-in-time supply chains demand reliability
Common Disruption Causes
• Adverse weather conditions
• Port congestion and labour strikes
• Mechanical failures
• Geopolitical disturbances
Trans-Pacific Case Study Route
KWY
Kwangyang ← Origin
↓
BUS
Busan
↓
QIN
Qingdao
↓
NAG
Nagoya
↓
YOK1
Yokohama (out)
↓
LGB
Long Beach
↓
OAK
Oakland
↓
DHB
Dutch Harbor
↓
YOK2
Yokohama (ret)
↓
KWY2
Kwangyang ← Sink

## Slide 4
Recovery Strategies
Four strategy types, applied individually or in combination
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Speed Adjustment
SLOW 15kn / NORMAL 20kn / FAST 25kn
Fuel cost ∝ v²·d (cubic model) Fast speed recovers time at high fuel cost
Expedited Handling
STANDARD 12h → EXPEDITED 8h
Saves 4h per port call Additional resource cost: $200 vs $100
Port Omission
Skip one or more consecutive planned ports
Saves travel + handling time Penalty: $1,000 per omitted port
Port Swapping
Reorder two port visits (non-adjacent, max distance 2)
Three-leg swap group: Leg A → Leg B → Leg C Ordering variables enforce sequence consistency

## Slide 5
Mathematical Model
Mixed-Integer Program on a time-space network
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Objective Function
α ∈ [0,1] controls the service / cost trade-off
Decision Variables
1 if edge e sailed with duration mode d
1 if port p visited with duration mode d
1 if strategy s applied at port p
1 if container c arrives late
1 if container c misses connection
1 if port i visited before port j (swap ordering)
1 if swap group g is active
Key Constraint Groups
Flow conservation
Origin: Σ x = 1 | Sink: Σ x = 1 | Interior: flow in = flow out
Port-call consistency
for edges arriving at p
Swap group integrity
All 3 legs of group g active swap_active_g = 1
Ordering (antisymmetry)
for all interior pairs
Ordering (transitivity)
for all triples
Delay classification
Misconnection logic
for non-connecting transshipment edges

## Slide 6
Implementation Architecture
Solver-agnostic, modular, fully reproducible
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Experiments
benchmark.py
sensitivity.py
cfa.py
penalty_sensitivity.py
stochastic_ets.py
Model
xpress_solver.py
highs_solver.py
cbc_solver.py
mip_builder.py (PuLP)
Core
entities.py
network.py
costs.py
emissions.py
simulation.py
validation.py
Data
base_instance.py
instance_generator.py

## Slide 7
Port Swap: Three-Leg Group Mechanism
Brouer et al. (2013) extended to non-adjacent pairs
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Planned route:
YOK1(4)
→
LGB(5)
→
OAK(6)
→
DHB(7)
→
YOK2(8)
Leg A
YOK1(4) → DHB(7)
Vessel goes directly to DHB, skipping LGB Skipped: OAK(6) swap_group_id = 9
Leg B
DHB(7) → LGB(5)
Vessel backtracks to LGB after serving DHB Identifies swap pair: from > to swap_group_id = 9
Leg C
LGB(5) → YOK2(8)
Vessel resumes forward from LGB succ(DHB) = YOK2 swap_group_id = 9
Recovered route:
YOK1(4)
→
DHB(7)
→
LGB(5)
→
YOK2(8)
Enforcement constraints
• for each leg type (all-or-nothing integrity)
• (DHB visited before LGB when swap fires)
• (at most one swap in the entire route)
• (both ports classified PORT_SWAP)

## Slide 8
Emissions & Regulatory Compliance Model
Single-fuel VLSFO assumption — CO₂, EU ETS, IMO CII, FuelEU Maritime
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Cubic Fuel Model
F = F₀ · (v/v₀)³ · d/(v·24)
• F₀ = 100 t/day at v₀ = 20 kn
• Fuel cost ∝ v² · d (quadratic in speed)
• 15 kn uses 2.78× less fuel than 25 kn
• CO₂ = F × 3.114 (VLSFO emission factor)
EU ETS (Regulation EU 2023/957)
C_ETS = CO₂ × φ_year × P_carbon
• 2024: φ = 40% | 2025: φ = 70% | 2026+: φ = 100%
• Baseline carbon price: €65/tCO₂
• Stochastic: TN(65, 15², [30, 130]) in CFA
IMO CII (Carbon Intensity Indicator)
Attained = CO₂[g] / (DWT · distance)
Required = 1984 · DWT⁻⁰·⁴⁸⁹
A (≤0.85×req) B (≤0.95×) C (≤1.05×) D (≤1.15×) E (>1.15×)
Result: Rating A in all scenarios (attained/required ≈ 0.51)
FuelEU Maritime (corrected formula)
Penalty = (g−g*)/g · F_total · LHV / LHV · 2400 · FX
• g = 91.16 gCO₂eq/MJ (VLSFO, always non-compliant from 2025)
• g* ≈ 88.61 gCO₂eq/MJ (2026 limit, interpolated)
• LHV = 40,500 MJ/tonne (energy-based formula, corrected)
• Penalty ≈ €72.5/tonne fuel | VLSFO always non-compliant

## Slide 9
Alpha Sensitivity Analysis
How the cost–service trade-off shifts across α values
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Sharp transition at α=0.6
Operational cost jumps from ~$820k to ~$1,100k as model switches from swap+omission to fast full-visit routes
CO₂ increases with service focus
Emissions rise ~50% above α=0.6 — faster speeds to avoid delays burn significantly more fuel
5 → 0 delayed containers
Full range from maximum delay (α=0) to zero delay (α=0.7+) across the sweep

## Slide 10
Cost–Service Pareto Frontier
Each point is the optimal solution at a given α value
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Low α (0.0–0.2)
Operational cost ~$750k Service cost ~$515k 5 containers delayed, 3 ports skipped
Mid α (0.3–0.5)
Operational cost ~$820k Service cost ~$269k 3 delayed, swap activated
High α (0.6–0.9)
Operational cost ~$1,100k Service cost ~$0 0 delayed, fast full-visit routes

## Slide 11
Initial Delay Sensitivity Analysis
Recovery cost scales non-linearly with disruption severity
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Threshold at 36h
Objective jumps from $425k to $489k — second container crosses its promised arrival threshold
Plateau above 48h
Objective stabilises at $545k — same 3 containers always delayed. Promises calibrated to 48h expected delay.
Emissions dip at 36h
CO₂ drops as model switches to a more fuel-efficient route (different port omission), then recovers

## Slide 12
The Green Recovery Tension
Prioritising service increases emissions — a fundamental trade-off
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Key Insight: The Green Recovery Tension
• At α ≤ 0.5: slow steaming minimises fuel and CO₂ — but accepts container delays
• At α ≥ 0.6: fast speeds eliminate delays — but CO₂ increases by ~50% and ETS exposure rises proportionally
• FuelEU penalty = $0 throughout (flag=False) — under VLSFO, always non-compliant regardless of speed
• CII Rating A in all scenarios — slow steaming produces attained/required ratio of 0.51

## Slide 13
CII Profile and ETS Exposure
IMO CII Rating A across all scenarios — ETS cost linear in carbon price
TJL Optimization | VSRP Extensions & Benchmarking | 2026
CII Finding
Attained CII ≈ 3.65 gCO₂/(DWT·nm) across all delay scenarios. Required CII = 7.12. Ratio = 0.51 → Rating A in every scenario. Slow steaming (15 kn) dramatically reduces CO₂ per transport work unit. The CII reference line is calibrated to nominal-speed operations.
ETS Strategy Finding
Strategy mix (2 omissions + 1 swap) is invariant to carbon price. ETS carbon price does not enter the MIP objective — only FuelEU does. ETS cost is perfectly linear in carbon price: slope = 4,248 t CO₂ × 1.0 phase-in = 4,248 EUR per EUR/tCO₂. At €130/tCO₂ → ETS exposure reaches €552k per voyage.

## Slide 14
Solver Benchmark: Xpress vs HiGHS vs CBC
All three solvers find identical optimal solutions
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Solver
Avg Objective
Avg Runtime
MIP Gap
Feasible
Optimal
Xpress
$501,429
0.015s
0.0%
100%
100%
HiGHS
$501,429
0.050s
0.0%
100%
100%
CBC
$501,429
0.258s
0.0%
100%
100%
Solution quality
All three solvers find the same optimal objective — PuLP MIP builder produces identical formulation to Xpress
Speed advantage
Xpress is 3.3× faster than HiGHS and 17× faster than CBC on these instances
Solver independence
HiGHS and CBC operate with no Xpress dependency — PuLP exports to MPS format

## Slide 15
Cost Function Approximation — The Learning Loop
Powell (2022) framework: parametric optimisation + simulator + parameter update
TJL Optimization | VSRP Extensions & Benchmarking | 2026
1
Sample estimated delay μ_est = 48h, σ = 12h
→
2
Apply theta tightening to container promises
→
3
Solve MIP → fixed route
4
Sample realised scenario delay, weather, handling, prices
→
5
Simulate realised outcome which containers missed?
→
6
Update theta at ports with misses
↑ repeat for n_episodes ↑
Key asymmetry — why CFA works:
MIP sees tightened promises (theta applied) → solver builds in buffer → simulator evaluates against ORIGINAL promises → more containers arrive on time → theta updated to reinforce what worked

## Slide 16
Theta Evolution During Training
How each update rule learns to tighten container promises
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Observations
Additive:
QIN, LGB, YOK2 increase linearly. DHB slower (fewer misses). Never decreases.
Decay:
Same ports increase but DHB shows two-sided behaviour — rises with misses, falls without.
SPSA:
Jumps to cap (30h) at 6 ports in episode 1. Gradient-guided — finds optimal in one step.

## Slide 17
CFA Policy Performance
Realised metrics only — MIP objectives not directly comparable across policies
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Policy
Avg missed
Avg svc cost
vs Baseline
p95 tail risk
Baseline
4.00
$298,912
—
$346,477
Additive
3.60
$272,439
−8.9%
$339,030
Decay
3.70
$277,196
−7.3%
$339,030
SPSA
3.00
$243,900
−18.4%
$243,900
SPSA Key Result
−18.4% average service cost Zero variance: p90 = p95 = mean = $243,900 std = $0 Converges in 1 episode: Gradient-guided update identifies maximum tightening at 6 ports as optimal immediately. 3 MIP solves per update (1 main + 2 perturbations) vs 1 for additive/decay

## Slide 18
Tail Risk: SPSA Eliminates Worst-Case Scenarios
Distribution of realised service cost across 20 test episodes
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Baseline
Wide distribution p95=$346k, outlier at $485k Significant tail exposure
Additive & Decay
Similar to each other p95=$339k Modest improvement, tail unchanged
SPSA
Degenerate distribution All 20 episodes = $243,900 Zero variance, zero tail risk

## Slide 19
Regulatory Exposure by CFA Policy
FuelEU compliance and ETS cost across policies
TJL Optimization | VSRP Extensions & Benchmarking | 2026
FuelEU: 0% compliance — expected
Under single-fuel VLSFO, GHG intensity (91.16 gCO₂eq/MJ) always exceeds the 2026 FuelEU limit (88.61 gCO₂eq/MJ). Compliance requires switching to alternative fuels — outside current scope.
ETS: similar across policies
Average realised ETS cost: €274k–€278k across all policies. SPSA slightly higher (€277,703) because aggressive tightening forces faster routes that burn more fuel. Trade-off: −18.4% service cost vs +1.1% ETS exposure.

## Slide 20
Penalty Sensitivity Analysis
Swap and speed-up penalties swept across four random seeds
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Swap: objective increases linearly with penalty — route unchanged $0–$5,000
Speed-up: completely flat — fast speed never optimal for this container set

## Slide 21
Key Findings
TJL Optimization | VSRP Extensions & Benchmarking | 2026
①
Pareto frontier is non-linear
Two distinct regimes: swap-based recovery (α ≤ 0.5, ~$820k operational) and fast-speed full-visit recovery (α ≥ 0.6, ~$1,100k). The transition is sharp.
②
Green recovery tension is real
Prioritising service (α ≥ 0.6) increases CO₂ by ~50% and ETS exposure proportionally. Slow steaming achieves CII Rating A — but only when service quality is sacrificed.
③
All solvers find identical solutions
Xpress, HiGHS, and CBC all find the same optimal objective. Xpress is 3.3× faster than HiGHS and 17× faster than CBC.
④
SPSA dominates all CFA policies
−18.4% average service cost. Zero variance (p95 = mean = $243,900, std = $0). Converges in one episode via simultaneous gradient estimation.
⑤
Swap activation is demand-dependent
Swap activated in 2 of 4 seeds, robust to penalties up to $5,000. For other seeds, no swap is ever beneficial — confirms Brouer et al. (2013).

## Slide 22
Limitations and Future Work
TJL Optimization | VSRP Extensions & Benchmarking | 2026
Current Limitations
• Single-fuel VLSFO
FuelEU always non-compliant; no fuel-switching decisions possible
• Per-voyage FuelEU
Regulation is annual; per-voyage approximation is standard in literature
• Delay constraint approximation
Uses nominal speed on prior legs; big-M formulation would be exact
• Delay sweep plateau above 48h
Structural property of 5-container test set; more containers needed
• time_to_first_feasible
Unavailable on Xpress community license
• Swap rarely activates
Demand-dependent; larger instances with more containers needed to show broader activation
Natural Extensions
• Multi-fuel model
LNG/methanol switching variables; fuel-choice per leg
• Annual CII compliance
Multi-voyage constraint linking CII across the fleet
• Larger instances
25+ containers to show richer delay sweep variation and strategy diversity
• SPSA with diminishing step size
Theoretical convergence guarantees via a_k = a/(k+A)^α schedule
• Port hoteling emissions
Add at-berth emissions to the CO₂ accounting module

## Slide 23
References
TJL Optimization | VSRP Extensions & Benchmarking | 2026
1.
Brouer, B.D. et al. (2013). The Vessel Schedule Recovery Problem (VSRP).
European Journal of Operational Research, 224(2), 362–374.
2.
Li, S. et al. (2023). Vessel schedule recovery strategy in liner shipping.
Ocean and Coastal Management, 237, 106514.
3.
Hu, Liu, Jin, Wang (2024). Liner disruption recovery with emission control area policies.
Transportation Research Part D, 132, 104227.
4.
Zhou et al. (2024). Schedule recovery under ECA regulation.
Journal of Marine Science and Engineering.
5.
Li, S. & Wang, T. (2025). ETS effects on liner disruption recovery.
Transport Policy, 169, 191–208.
6.
Powell, W.B. (2022). Reinforcement Learning and Stochastic Optimization.
Wiley. [CFA framework]
7.
IMO MEPC.338(76) — CII reference lines for container ships.
8.
Regulation (EU) 2023/957 — EU ETS maritime phase-in schedule.
9.
FuelEU Maritime Regulation — GHG intensity limits and Article 23 penalty.

## Slide 24
Thank You
Vessel Schedule Recovery Problem Extensions, Benchmarking & Regulatory Compliance
Code: python -m scripts.smoke_test
Figures: results/figures/
Tables: results/tables/